## Slide 1
Computer Networks: Session 3
INAE Faculty Mentorship Program
Tarun Mangla
Assistant Professor,
Department of Computer Science & Engineering,
IIT Delhi
Notes: Today I'll talk about our work rethinking how we design speed tests. Speed tests are everywhere — billions are run every year by consumers, operators, regulators, researchers. But despite all that usage, the tools haven't kept up with what stakeholders actually need. I'll argue we should move beyond one-shot bandwidth numbers toward lightweight, diagnostic, longitudinal measurement.

## Slide 2: Recap
Overview of the Internet
  Architecture, performance metrics, socket programming, switched networks, decentralization, packet-switching
Pedagogy
  Bottom-up vs top-down
  In-class exercises, quizzes
  Building from first principles
  Design trade-offs and not “facts”
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
Ht
Hn
M
segment
Ht
datagram
destination
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
M
Ht
Hn
Hl
M
router
switch
message
M
Ht
M
Hn
frame
link
physical

## Slide 3: Today’s Session: Routing
How to route data?
  within an L2-switched network (l2 routing)
  within a single network (intra-domain routing)
  across networks (inter-domain routing)

## Slide 4: What is the first thing needed for routing?
Address: identifier for the host machines
  Routing is destination-lookup based
Internet has two types of addresses
  MAC addresses: used in the link layer
  IP addresses: used in the network layer
MAC address:
  Completely “flat” 48-bit number
  For example: 00:40:05:1c:0e:9f
IP address
  Hierarchical 32-bit number for IPv4
  For example: 8.8.8.8
  Each subnetwork has a prefix

## Slide 5: Routing and Forwarding
Each switch has multiple physical ports
  Packet comes to an input port
  Forwarded to an output port based on the destination
Forwarding
(data plane)
Move a frame from an input port to the appropriate output port
Uses a forwarding table: destination address → output port
Routing
(control plane)
Determine the forwarding table using routing algorithms
Network-wide, cooperative process (seconds–minutes)
Two key functions

## Slide 6: L2 Routing
Option 1: Using static tables added by network administrator
  Difficult to support dynamic addition of nodes (end-hosts and switches)
Option 2: Using a centralized node
  Method: Each switch registers with the node and the node computes the forwarding table
Option 3: Distributed algorithms
  Each switch constructs the routing table independently
  Messages are exchanges for sharing information about neighbors/hosts

## Slide 7: Routing algorithm: Self-learning Switch
A
A’
B
B’
C
C’
1
2
3
4
5
6
switch learns which hosts can be reached through which interfaces
A A’
Source: A
Dest: A’
MAC addr interface TTL
Switch table
(initially empty)
A
1
60
  when frame received, switch “learns” location of sender: incoming LAN segment
  records sender/location pair in switch table

## Slide 8: Self-learning switch
A
A’
B
B’
C
C’
1
2
3
4
5
6
A A’
Source: A
Dest: A’
MAC addr interface TTL
switch table
(initially empty)
A
1
60
A A’
A A’
A A’
A A’
A A’
A’ A
A’
4
60
frame destination, A’, location unknown:
flood
destination A location known:
selectively send
on just one link
switch learns which hosts can be reached through which interfaces

## Slide 9: L2 Routing: Self-learning Switch
when frame received at switch:
  1. record incoming link, MAC address of sending host
  2. index switch table using MAC destination address
  3. if entry found for destination then {
  if destination on segment from which frame arrived then drop frame
  else forward frame on interface indicated by entry
  }
  else flood /* forward on all interfaces except arriving interface */

## Slide 10: Interconnecting switches
self-learning switches can be connected together:
Self learning! (works exactly the same as in single-switch case!)
Q: show switch tables and packet forwarding in S1, S2, S3, S4
A
B
S1
C
D
E
F
S2
S4
S3
H
I
G
1
2
3
1
2
3
1
2
3
1
2
3

## Slide 11: What happens in case of a loop?
When host A sends a packet to B, the packets will circulate forever inside the network on all the switches because they forward it indefinitely
How do we prevent packets from looping?

## Slide 12: Break the Loop (Logically)
Idea: All nodes should be connected but there should be no cycles
  Spanning tree: subgraph that covers all vertices but contains no cycles
  Switches will only forward on ports lying on the spanning tree
Requirement: distributed algorithm
  Challenge: How to create the same spanning tree in a distributed manner
How to create the spanning tree?

## Slide 13: Distributed Spanning Tree Algorithm: Key Idea
All switches pick a common “root” switch — whichever has the lowest Ethernet address (assumes unique addresses)
All other switches select the shortest path to that root switch; any links not on the shortest path of at least one switch are removed
Tie-break: pick the hop with the lower MAC address
If information is stale, timeout so that if a link fails a different tree is chosen

## Slide 14: STP (Details)
Initially, each switch thinks it is the root
  Tell its neighbors that I have a path to the root (me) with 0 hops
  When receives message from a smaller switch ID, stop generating own configuration messages

## Slide 15: STP (Details)
Initially, each switch thinks it is the root
  Tell its neighbors that I have a path to the root (me) with 0 hops
  When receives message from a smaller switch ID, stop generating own configuration messages
If someone else is the root
  Keep track of the shortest path to X that anyone has advertised
  Tell all my neighbors except the one with better path about this shortest path to X
  If someone else advertises a path to X that is shorter than mine, update my idea of a shortest path. Re-advertise

## Slide 16: Spanning Tree Protocol
Fun fact: Invented by Radia Perlman from Digital Equipment Corporation (DEC)

## Slide 17: Question: Spanning Tree Algorithm and Performance
Does the spanning tree algorithm find optimal path?

## Slide 18
5 minutes
Break

## Slide 19: Performance of Spanning Tree Protocol
The spanning tree protocol + flooding-based routing is designed to support extremely simple forwarding switches.
  It does not focus on performance at all
Can we design better routing algorithms?
What do we mean by “better”?

## Slide 20: Two Types of Routing
Routing domain: An internetwork where all the routers are under the same administrative control (e.g., university campus or an ISP)
Intra-domain routing: routing packets within a domain
  Simpler routing policy under one administrative domain
  Shorter or faster paths  better routes
Inter-domain routing: routing packets across multiple domains
  E.g., across IITD and NKN network
  Involve complex policies driven by economics

## Slide 21: Intra-domain Routing: Graph Abstraction
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
graph: G = (N,E)
ca,b: cost of direct link connecting a and b
e.g., cw,z = 5, cu,z = ∞
cost defined by network operator: could always be 1, or inversely related to bandwidth, or inversely related to congestion
N: set of routers = { u, v, w, x, y, z }
E: set of links ={ (u,v), (u,x), (v,x), (v,w), (x,w), (x,y), (w,y), (w,z), (y,z) }
How to determine shortest path from one node to all other nodes in a graph?
Routing is to find the lowest-cost path between any two nodes
Cost of a path == Sum of the costs of all the edges that make up the path

## Slide 22: Why not use static routing?
One might calculate all shortest paths and load them into routers
Problems:
Alternatives: dynamic and/or distributed protocol
  Distance vector
  Link state

## Slide 23: Distance vector algorithm
Based on Bellman-Ford (BF) equation (dynamic programming):
Suppose that u’s neighboring nodes, x,v,w, know that for destination z:
u
y
z
2
2
1
3
1
1
2
5
3
5
Dv(z) = 5
v
Dw(z) = 3
w
Dx(z) = 3
x

## Slide 24: Distance vector algorithm
key idea:
Every T seconds, each router sends its own distance vector estimate to neighbors
under minor, natural conditions, the estimate Dx(y) converge to the actual least cost dx(y)
Dx(y) ← minv{cx,v + Dv(y)} for each node y ∊ N
when x receives new DV estimate from any neighbor, it updates its own DV using BF equation:

## Slide 25: Distance vector: Example

## Slide 26: Good News Travels Fast, Bad News Travels Slow!
Assume a new node F comes up in the network
How long does it take for the A to update their routing table?
In general, good news spreads at rate of one hop per exchange
  What is the maximum time it can take?
What happens in case of link failure?

## Slide 27: Count-to-infinity Problem
A
B
C
✕
cost=1
cost=1
A-B link DOWN → B cannot directly reach A
Node B — Routing Table
Node C — Routing Table
Round 0: Initial (before failure)
Dest
Cost
Next
B
0
—
A
1
A
Round 0: Initial (before failure)
Dest
Cost
Next
B
1
B
A
2
B
Round 1: A-B link down — B detects
Dest
Cost
Next
B
0
—
A
∞
—
Round 1: A-B link down — B detects
Dest
Cost
Next
B
1
B
A
2
B
Round 2: C advertises → B updates
Dest
Cost
Next
B
0
—
A
3
C
Round 2: C advertises → B updates
Dest
Cost
Next
B
1
B
A
2
B
Round 3: B advertises → C updates
Dest
Cost
Next
B
0
—
A
3
C
Round 3: B advertises → C updates
Dest
Cost
Next
B
1
B
A
4
B
Round 4: C advertises → B updates
Dest
Cost
Next
B
0
—
A
5
C
Round 4: C advertises → B updates
Dest
Cost
Next
B
1
B
A
4
B
Round 5: B advertises → C updates
Round 5: B advertises → C updates
A
∞
—
A
∞
—
Each round cost(A) grows by 1 (B: 1→∞→3→5→∞, C: 2→2→4→6→∞) — neither node learns the link is truly broken

## Slide 29: How to Handle Count to Infinity Problem?
Split horizon
  Don’t announce the route back to the next hop
  Does it always work?

## Slide 30: How to Handle Count to Infinity Problem?
Split horizon
  Don’t announce the route back to the next hop
  Does it always work?

## Slide 31: How to Handle Count to Infinity Problem?
Split horizon
  Don’t announce the route back to the next hop
Make infinity smaller
  Routing Information Protocol (RIP): Based on hop count
  Used a maximum length of 15
  Limitation: Doesn’t work for cases when actual path length is greater than 15

## Slide 32: RIP Message Format
RIPv2 Protocol Message Format

## Slide 33: Distance Vector: Summary
Building a routing table by distributing vector of distances to neighbors
Completely distributed and based only on knowledge of immediate neighbors
  Simpler computation, small update message size
  Slow convergence
Count to infinity problem and limited network diameter
  Used in small-sized networks (E.g., LAN or private wide-area networks)

## Slide 34: Link State Routing Algorithm
Each node knows the entire network topology including link costs:
  accomplished via “link state broadcast”
  all nodes have same info
Link state broadcast:
  (x, {list of neighbors, cost}, seq #, TTL)
  reliable broadcast using acknowledgements
Once a node has the entire topology:
  Use Dijkstra’s algorithm to find the shortest path

## Slide 35: Reliable Flooding
Goal: Ensure every node have most recent LSP from each node
Forward LSP to all nodes but one that sent it
Send an acknowledgment back to the sending node
Retransmit the LSP if an acknowledgment is not received within a certain time frame
Generate new LSP periodically; increment SEQNO. This helps routers compare updates to determine the newer one
Start SEQNO at 0 when reboot (this creates a host of issues we’ll ignore)
Discard old LSPs after a timeout (e.g. 1 hour)

## Slide 36: Dijkstra’s link-state routing algorithm
1 Initialization:
2 N' = {u} /* compute least cost path from u to all other nodes */
3 for all nodes v
4 if v adjacent to u /* u initially knows direct-path-cost only to direct neighbors */
5 then D(v) = cu,v /* but may not be minimum cost! */
6 else D(v) = ∞
7
8 Loop
9
10
11
12
13
14
15 until all nodes in N'
find w not in N' such that D(w) is a minimum
add w to N'
update D(v) for all v adjacent to w and not in N' :
D(v) = min ( D(v), D(w) + cw,v )
/* new least-path-cost to v is either old least-cost-path to v or known
least-cost-path to w plus direct-cost from w to v */

## Slide 37: Dijkstra’s algorithm: an example
D(w),p(w)
5,u
4,x
3,y
3,y
Step
0
1
2
3
4
5
N'
D(v),p(v)
D(x),p(x)
D(y),p(y)
D(z),p(z)
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
D(w),p(w)
v
w
x
y
z
Two popular link state routing protocols: Intermediate System to Intermediate System (IS-IS), Open Shortest Path First (OSPF)

## Slide 38: Takeaways
L2: learn MACs, flood the unknown, spanning tree breaks loops — no shortest path.
L3 routing: a distributed shortest-path computation over the router graph.
Distance vector: know only neighbors. Cheap, but slow convergence and count-to-infinity.
Link state: flood the topology, run Dijkstra locally. Fast and loop-free, more overhead.
Trade-off: local vs. global knowledge — RIP/EIGRP vs. OSPF/IS-IS.
Distributed protocols at the heart of routing

## Slide 39: Common Misconceptions Among Students