## Slide 1
Computer Networks: Session 4
INAE Faculty Mentorship Program
Tarun Mangla
Assistant Professor,
Department of Computer Science & Engineering,
IIT Delhi
Notes: Today I'll talk about our work rethinking how we design speed tests. Speed tests are everywhere — billions are run every year by consumers, operators, regulators, researchers. But despite all that usage, the tools haven't kept up with what stakeholders actually need. I'll argue we should move beyond one-shot bandwidth numbers toward lightweight, diagnostic, longitudinal measurement.

## Slide 2: Routing Recap

## Slide 3: Today’s Session: Routing
How to route data across networks?
Building a centralized control plane?

## Slide 4: Inter-domain routing
How does Internet route packet from x to y?
What you need:
Common addressing scheme
Common routing protocol

## Slide 5: Internet addressing or IP address
IP address: 32-bit identifier associated with each host or router interface
dotted-decimal IP address notation:
How does an AS obtain IP address?
  Need a coordinating agency
  Internet Assigned Numbers Authority (IANA) and Internet Corporation for Assigned Names and Numbers (ICANN)
103.27.10.1 = 01100111 00011011 00001010 00000001
103
27
1
10
Notes: -

## Slide 6: IP addresses are hierarchical
103.27.10.4
103.27.10.3
103.27.10.1
103.27.11.1
103.27.11.3
103.27.11.2
103.27.9.2
103.27.9.1
103.27.9.3
103.27.10.2
IP addresses have a hierarchical structure:
  subnet part: all devices in the same subnet share the same high-order bits
  host part: remaining low-order bits, unique within the subnet
Why is it useful?
Notes: Few observations
Each router interface has one IP address.
Router entry can be 223.1.2.2 /
Can we do better?
Subnet mask . Either write it as 255.255.255.0 or 103.27.10.0/24

## Slide 7: Question: How many Subnets?
where are the subnets?
what are the /24 subnet addresses?
how many subnets?
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.2
223.1.2.6
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.2
223.1.7.0
223.1.7.1
223.1.8.0
223.1.8.1
223.1.9.1
223.1.9.2
223.1.2.1
subnet 223.1.1/24
subnet 223.1.7/24
subnet 223.1.3/24
subnet 223.1.2/24
subnet 223.1.9/24
subnet 223.1.8/24

## Slide 8: Why 4 dotted representation of IP addresses?
In the beginning, IP addresses were divided into 5 categories, called classful addressing
  Classes: A, B, C, D, and E
Advantages: Hierarchical routing
Notes: Class

## Slide 9: Limitations of Classful Addressing
Wastage of IP address space due to fixed class sizes
Large routing tables increase router overhead
Inflexible — only three class sizes (A, B, C) available
Accelerated exhaustion of the IPv4 address space

## Slide 10: Example: IP Addresses of two AS

## Slide 11: CIDR: Classless InterDomain Routing (pronounced “cider”)
  subnet portion of address of arbitrary length
  address format: a.b.c.d/x, where x is # bits in subnet portion of address
11001000 00010111 00010000 00000000
subnet
part
host
part
200.23.16.0/23

## Slide 12: Inter-AS routing
How does Internet route packet from x to y?
What are the requirements for inter-AS routing?
Common addressing scheme
Common routing protocol

## Slide 13: Internet inter-AS routing
Can we use link-state or distance-vector?
scale: millions of destinations/routers
autonomy: ASes don’t want to expose internal topology
policy: each AS wants to control how traffic is routed through it
BGP (Border Gateway Protocol): the de facto inter-domain routing protocol
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS 2
AS 3
AS 1
Notes: Since an inter-AS routing protocol involves coordination among multiple ASs, communicating ASs must run the same inter-AS routing protocol. In fact, in the Internet, all ASs run the same inter-AS routing protocol, called the Border Gateway Protocol, more commonly known as BGP

## Slide 14: What is Border Gateway Protocol (BGP)
Each AS has one or more speakers that advertise BGP routes
BGP routers communicate via TCP for reliable delivery
Advertisements are of the form: If you send packets to me, I can send them to 82.128.0.0/9 through the path AS4123, AS1045, AS9
  Two important attributes: AS-PATH and NEXT-HOP
  path vector protocol
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS 2
AS 3
AS 1

## Slide 15: BGP Example
ASes advertise routes to each other
An AS may have received multiple advertisements to the same IP address
Once it has picked a route, it starts sending packets over that route and advertises the others and withdraws previous routes if any
To a given AS B, AS A will advertise only one route to any prefix X. Exception is if the ASes are connected via multiple routers, in which case it can send one advertisement per connection point

## Slide 16: BGP Example
ASes advertise routes to each other
An AS may have received multiple advertisements to the same IP address
Once it has picked a route, it starts sending packets over that route and advertises the others and withdraws previous routes if any
To a given AS B, AS A will advertise only one route to any prefix X. Exception is if the ASes are connected via multiple routers, in which case it can send one advertisement per connection point

## Slide 17: BGP Example: What if there is a loop in the network?

## Slide 18: BGP path advertisement: multiple paths
AS2,AS3,X
AS1 gateway router 1c learns path AS2,AS3,X from 2a
gateway router may learn about multiple paths to destination:
AS3,X
AS1 gateway router 1c learns path AS3,X from 3a
How does AS1 decide which is the best path?
AS3, X
2b
2d
2c
2a
AS 2
3b
3d
3c
3a
AS 3
1b
1d
1c
1a
AS 1
X

## Slide 19: Inter-AS Routing: Policies
No transit traffic through certain ASes
Never put China on a route starting from Ministry of Defence
Do not use Singapore to get from India to Maldives
Traffic starting or ending at Google should not transit through Microsoft
Don’t share information about this peering link to other routers
Set local preference on BGP routes

## Slide 20: What happens if local pref is the same?
2b
2d
2c
2a
AS 2
3b
3d
3c
3a
AS 3
1b
1d
1c
1a
AS 1
X
2d learns (via iBGP) it can route to X via 2a or 2c
Shortest AS path length
hot potato routing: choose local gateway that has least intra-domain cost (e.g., 2d chooses 2a, even though more AS hops to X): don’t worry about inter-domain cost!
AS3,X
AS1,AS3,X
201
112
263

## Slide 21: BGP route selection rules
Router may learn about more than one route to destination AS, selects route based on:
  local preference value attribute: policy decision
  shortest AS-PATH
  closest NEXT-HOP router: hot potato routing
  additional criteria

## Slide 22: BGP: achieving policy via selective advertisements
A advertises path Aw to B and to C
B chooses not to advertise BAw to C!
  B gets no “revenue” for routing CBAw, since none of C, A, w are B’s customers
  C does not learn about CBAw path
C will route CAw (not using B) to get to w
ISP only wants to route traffic to/from its customer networks (does not want to carry transit traffic between other ISPs – a typical “real world” policy)

## Slide 23: Policy via Selective Advertisements

## Slide 24: Connecting Intra- and Inter-domain Routing

## Slide 25: Recap
Looked at three kinds of routing protocols: L2 routing, intra-domain routing, and inter-domain routing
All are distributed algorithms — running independently on each router
Advantages: generally resilient and scalable
However, there are also limitations …

## Slide 27: Traffic engineering: difficult with traditional routing
2
2
1
3
1
1
2
5
3
5
v
w
u
z
y
x
Q: what if network operator wants u-to-z traffic to flow along uvwz, rather than uxyz?
A: need to re-define link weights so traffic routing algorithm computes routes accordingly (or need a new routing algorithm)!
Indirect control: Changing weights instead of paths

## Slide 28: Traffic engineering: difficult with traditional routing
2
2
1
3
1
1
2
5
3
5
v
w
u
z
y
x
Q: what if network operator wants to split u-to-z traffic along uvwz and uxyz (load balancing)?
A: can’t do it (or need a new routing algorithm)
Lack of flexibility!

## Slide 29: Traditional Router: Per-router distributed control plane
high-speed
switching
fabric
routing
processor
router input ports
router output ports
forwarding data plane
routing, management
control plane (software)
Limitation: Traffic management is challenging with a distributed control plane

## Slide 30: Idea of Software Defined Networks

## Slide 31: (Logically) Centralized Controller
Controller Platform

## Slide 32: A Helpful Analogy: Computer Systems (From Nick McKeown’s talk “Making SDN Work” at the Open Networking Summit, April 2012)
Vertically integrated
Closed, proprietary
Slow innovation
Small industry
Specialized
Operating
System
Specialized
Hardware
App
App
App
App
App
App
App
App
App
App
App
Specialized
Applications
Horizontal
Open interfaces
Rapid innovation
Huge industry
Microprocessor
Open Interface
Linux
Mac
OS
Windows
(OS)
or
or
Open Interface

## Slide 33: Network Elements
Vertically integrated
Closed, proprietary
Slow innovation
App
App
App
App
App
App
App
App
App
App
App
Horizontal
Open interfaces
Rapid innovation
Control
Plane
Control
Plane
Control
Plane
or
or
Open Interface
Specialized
Control
Plane
Specialized
Hardware
Specialized
Features
Merchant
Switching Chips
Open Interface
How does such a software-defined network look?
Notes: Broadcom, Intel

## Slide 34: Software-defined Network Architecture

## Slide 35: OpenFlow: An SDN Architecture Example
OpenFlow API
  API used to specify generalized forwarding actions
Three classes of OpenFlow messages:
  controller-to-switch
  asynchronous (switch to controller)
  symmetric (misc.)
OpenFlow Controller

## Slide 36: OpenFlow API
flow: defined by header field values (in link-, network-, transport-layer fields)
generalized forwarding: simple packet-handling rules
  match: pattern values in packet header fields
  actions: for matched packet: drop, forward, modify, matched packet or send matched packet to controller
  priority: disambiguate overlapping patterns
  counters: #bytes and #packets
Router’s flow table define router’s match+action rules
Flow table
match
action

## Slide 37: OpenFlow API
Match
Action
Stats
Forward packet to port(s)
Drop packet
Modify fields in header(s)
Encapsulate and forward to controller
Packet + byte counters
Header fields to match:
Ingress Port
Src MAC
Dst MAC
Eth Type
VLAN
ID
IP
ToS
IP Proto
IP Src
IP Dst
TCP/UDP Src Port
VLAN
Pri
TCP/UDP Dst Port
Link layer
Network layer
Transport layer

## Slide 38: OpenFlow: examples
IP datagrams destined to IP address 51.6.0.8 should be forwarded to router output port 6
Block (do not forward) all datagrams destined to TCP port 22 (ssh port #)
Block (do not forward) all datagrams sent by host 128.119.1.1
Destination-based forwarding:
*
*
*
*
*
*
51.6.0.8
*
*
*
port6
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
s-port
TCP
d-port
Action
VLAN
Pri
IP
ToS
*
*
*
*
*
*
*
*
*
*
*
*
Firewall:
drop
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
s-port
TCP
d-port
Action
VLAN
Pri
IP
ToS
22
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
s-port
TCP
d-port
Action
VLAN
Pri
IP
ToS
*
*
*
*
*
*
*
*
*
*
drop
*
128.119.1.1

## Slide 39: OpenFlow: controller-to-switch messages
Key controller-to-switch messages
features: controller queries switch features, switch replies
configure: controller queries/sets switch configuration parameters
modify-state: add, delete, modify flow entries in the OpenFlow tables
packet-out: controller can send this packet out of specific switch port
OpenFlow Controller

## Slide 40: OpenFlow: switch-to-controller messages
Key switch-to-controller messages
packet-in: transfer packet (and its control) to controller. See packet-out message from controller
flow-removed: flow table entry deleted at switch
port status: inform controller of a change on a port.
OpenFlow Controller