## Slide 1
Computer Networks: Session 2
INAE Faculty Mentorship Program
Tarun Mangla
Assistant Professor,
Department of Computer Science & Engineering,
IIT Delhi
Notes: Today I'll talk about our work rethinking how we design speed tests. Speed tests are everywhere — billions are run every year by consumers, operators, regulators, researchers. But despite all that usage, the tools haven't kept up with what stakeholders actually need. I'll argue we should move beyond one-shot bandwidth numbers toward lightweight, diagnostic, longitudinal measurement.

## Slide 2: Session Expectations
Not a course on networks — a course on teaching networks
Case studies and discussion, not lectures
Everyone contributes
  More fun
  Your question is probably someone else's too

## Slide 3: Recap
Overview of the Internet
  switched networks, decentralization for scale and resiliency, 3-tiered Internet structure, packet switching vs circuit switching
Pedagogy
  Design from first principles
  Focusing on the why and design trade-offs

## Slide 4: Today’s session: How to design and implement Internet?
Common Network Services
Data transmission (encoding, decoding)
Reliability
Addressing/routing
Congestion control
In-order delivery
..
Network structure
Given this long list of services and components, thinking about the architecture might be one way to go about it.

## Slide 5: What do we mean by architecture and why is it needed?
Architecture = a working model of a system
Descriptive: captures the current system
Prescriptive: guides how it evolves over time
In a systems context
Specify the modules that make up the system
Specify the interfaces between those modules
Why it matters
Separates what a module does from how it does it
Enables modules to evolve independently
Notes: Analogy: architecture of a house
Specifies functional components (rooms, layout)
Specifies interfaces (doors, connections)
Does not specify materials or finishes

## Slide 6: How do we reason about Internet architecture?

## Slide 7: Implementing layers through encapsulation
Every layer adds its own headers to the data. On the other end, every layer removes its headers

## Slide 8: Today’s Internet Architecture
application: supporting network applications
transport: process-process data transfer
network: routing of datagrams from source to destination
link: data transfer between neighboring network elements
physical: bits “on the wire”
link
application
network
transport
physical
application
transport
network
link
physical

## Slide 9: Different protocols in each layer
application: supporting network applications
  HTTP, IMAP, SMTP, DNS, FTP
transport: process-process data transfer
  TCP, UDP
network: routing of datagrams from source to destination
  IP, routing protocols
link: data transfer between neighboring network elements
  Ethernet, 802.11 (WiFi), PPP
physical: bits “on the wire”
link
application
network
transport
physical
application
transport
network
link
physical

## Slide 10: Layering and encapsulation
source
transport-layer protocol encapsulates application-layer message, M, with transport layer-layer header Ht to create a transport-layer segment
  Ht used by transport layer protocol to implement its service
application
transport
network
link
physical
destination
application
transport
network
link
physical
Transport-layer protocol transfers M (e.g., reliably) from one process to another, using services of network layer
Ht
M
Application exchanges messages to implement some application service using services of transport layer
M

## Slide 11: Services, Layering and Encapsulation
source
Transport-layer protocol transfers M (e.g., reliably) from one process to another, using services of network layer
Ht
M
network-layer protocol encapsulates transport-layer segment [Ht | M] with network layer-layer header Hn to create a network-layer datagram
  Hn used by network layer protocol to implement its service
application
transport
network
link
physical
destination
M
application
transport
network
link
physical
M
Ht
Hn
Network-layer protocol transfers transport-layer segment [Ht | M] from one host to another, using link layer services

## Slide 12: Services, Layering and Encapsulation
source
Ht
M
link-layer protocol encapsulates network datagram [Hn| [Ht |M], with link-layer header Hl to create a link-layer frame
application
transport
network
link
physical
destination
M
application
transport
network
link
physical
M
Ht
Hn
Link-layer protocol transfers datagram [Hn| [Ht |M] from host to neighboring host, using network-layer services
M
Ht
Hn
Hl
M
Ht
Hn
Network-layer protocol transfers transport-layer segment [Ht | M] from one host to another, using link layer services

## Slide 13: Services, Layering and Encapsulation
source
application
transport
network
link
physical
destination
application
transport
network
link
physical
M
Ht
Hn
Hl
M
Ht
Hn
Ht
M
M
M
message
Ht
M
segment
M
Ht
Hn
datagram
frame
M
Ht
Hn
Hl

## Slide 14: End-to-end overview of Internet Architecture
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
source
Ht
Hn
M
segment
Ht
datagram
destination
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
M
Ht
Hn
Hl
M
router
switch
message
M
Ht
M
Hn
frame
link
physical
Not all nodes will implement all the layers.

## Slide 15: An alternative Internet Architecture
OSI/ISO reference model
Two layers not found in Internet protocol stack!
  presentation: allow apps to interpret data (encryption, compression, conventions)
  session: synchronization, checkpointing, recovery of data exchange
application
presentation
session
transport
network
link
physical
The seven layer OSI/ISO
reference model
Design and implementation are not a linear process.
OSI 7-layer model was proposed but never saw the light of day — TCP/IP won in practice.
NEVER ADOPTED

## Slide 16: Where to implement network functions?
Common Network Services
Data transmission (encoding, decoding)
Reliability
Addressing/routing
Congestion control
In-order delivery
..
link
application
network
transport
physical
application
transport
network
link
physical

## Slide 17: Where to Implement Network Services?
In-network support
Network with rich functionality that covers most requirements
Complex switch design
  For example, switches implement reliability
End-system support only
As little functionality as possible in the network
Most functionality at the end points
  Dumb network, intelligent end-points
Two different paradigms

## Slide 18: Dumb Network, Intelligent End-hosts: End-to-end principle
Need end-to-end correctness anyways
Not everyone needs it
  Diminishing returns from in-network functionality
  Cost-effective
Not everyone has it
  All networks are not capable of providing functionalities
Flexibility of implementation
  Easier to change the end-hosts than all the switches in the network
Any limitations?

## Slide 19: Internet Protocol Graph
The internet protocol suite forms an hourglass: many applications (FTP, HTTP, DNS, TFTP) ride on TCP or UDP, which both narrow to a single waist — IP — that runs over any underlying network (NET₁…NETₙ). The right-hand stack shows the same idea as layers: Application → TCP/UDP → IP → Subnetwork.

## Slide 20: Summary
# 1: Layering, a useful construct, to organize Internet architecture
  Allows different implementations to inter-operate with each other
  Internet uses a 5-layered architecture, called IP stack
  Encapsulation used for adding layer information
#2: End-to-end principle
  Move all intelligence to the end hosts
  Makes the design of network simpler
  End hosts are easier to change compared to changing the entire network

## Slide 21
5 minutes
Break

## Slide 22: How do we measure the performance of a network?​
Why should we measure network?
What are the different metrics that characterize network performance?
Latency
Throughput
Loss

## Slide 23: Sources of packet delay
A
B
Notes: dproc: nodal processing
check bit errors
determine output link
typically < microsecs
dqueue: queueing delay
time waiting at output link for transmission
depends on congestion level of router
dprop: propagation delay:
time taken for the signal to reach its destination
d: length of physical link
s: propagation speed (~2x108 m/sec)
dprop = d/s
dtrans: transmission delay:
time taken to transmit the packet from host to the link
L: packet length (bits)
R: link transmission rate (bps)
dtrans = L/R

## Slide 24: Problem
d = 30,000 km Packet size = 1,000 bits Signal speed = 3 × 10⁸ m/s
Q: How long does it take to send a packet from A to B?

## Slide 25: Packet queueing delay (revisited)
a: average packet arrival rate
L: packet length (bits)
R: link bandwidth (bit transmission rate)
La/R ~ 0: avg. queueing delay small
La/R -> 1: avg. queueing delay large
La/R > 1: more “work” arriving is more than can be serviced - average delay infinite!
La/R ~ 0
La/R -> 1
traffic intensity = La/R
average queueing delay
1
service rate of bits
R
arrival rate of bits
L
a
.
:
“traffic
intensity”

## Slide 26: End-to-end delay
What is end-to-end delay?

## Slide 27: How do you measure delay on network?
  Ping: provides delay measurement from source to a destination
  traceroute program: provides delay measurement from source to router along end-end Internet path towards destination. For all i:
    sends three packets that will reach router i on path towards destination (with time-to-live field value of i)
    router i will return packets to sender
    sender measures time interval between transmission and reply
3 probes
3 probes
3 probes

## Slide 28: Throughput
throughput: rate (bits/time unit) at which bits are being sent from sender to receiver
  instantaneous: rate at given point in time
  average: rate over longer period of time
server, with
file of F bits
to send to client
link capacity
Rs bits/sec
link capacity
Rc bits/sec
server sends bits
(fluid) into pipe
pipe that can carry
fluid at rate
(Rs bits/sec)
pipe that can carry
fluid at rate
(Rc bits/sec)

## Slide 29: Throughput: network scenario
10 connections (fairly) share backbone bottleneck link R bits/sec
Rs
Rs
Rs
Rc
Rc
Rc
R
per-connection end-end throughput: min(Rc,Rs,R/10)
in practice: Rc or Rs is often bottleneck

## Slide 30: How do you measure end-to-end throughput on network?
Various speed test tools (e.g., ookla speedtest, mlab ndt7, iperf)
How does a speedtest work?
Let’s take a speedtest

## Slide 31: What is the official unit of energy?

## Slide 32: In a packet-switched network w/ each link having a bandwidth 100 kbps. What is the end-to-end transmission delay for sending 1 kbit data?

## Slide 33: Which statement is NOT true for packet switching.

## Slide 34: Congestion control needs to be implemented in a circuit-switched network

## Slide 35: And the winner is... 🥁

## Slide 36: How to teach rest of networking?
Bottom-Up
Physical → Application (Tanenbaum)
Pros
Mirrors how networks were engineered
Builds deep appreciation for L1/MAC fundamentals
Cons
Dry start; weak motivation
Apps and "why" come too late
Top-Down
Application → Physical (Kurose & Ross)
Pros
Grounded in apps students use daily
Socket programming early builds confidence
Cons
Lower layers feel like "magic"
Physical-layer topics get rushed
link
application
network
transport
physical
application
transport
network
link
physical

## Slide 37: Writing a networked application
socket: software endpoint where a process sends and receives data over the network
socket analogous to door
  sending process shoves message out door
  sending process relies on transport infrastructure on other side of door to deliver message to socket at receiving process
  two sockets involved: one on each side
Internet
controlled
by OS
controlled by
app developer
transport
application
physical
link
network
process
transport
application
physical
link
network
process
socket

## Slide 38: Socket Program
● ● Server (TCP)
import socket
s = socket.socket(socket.AF_INET,
socket.SOCK_STREAM)
s.bind(('', 12000))
s.listen(1)
# wait for a client
conn, addr = s.accept()
data = conn.recv(1024).decode()
reply = data.upper()
conn.send(reply.encode())
conn.close()
● ● Client (TCP)
import socket
s = socket.socket(socket.AF_INET,
socket.SOCK_STREAM)
s.connect(('localhost', 12000))
# send a line to the server
msg = input('Enter message: ')
s.send(msg.encode())
reply = s.recv(1024).decode()
print('From server:', reply)
s.close()

## Slide 39: Key Takeaways
The internet is built on layering and the end-to-end principle
  Protocols define services; layers hide complexity from those above
  Keep the network simple; put intelligence at the endpoints
Performance has a few core knobs
  Bandwidth, latency, jitter, loss — different apps care about different ones
Top-down vs bottom-up are teaching choices, not truths
  Pick the order that gets students to “why” fastest
Sockets are where the abstractions meet code
  Tutorial will work through socket programming hands-on
Next session: addressing and routing